## Slide 1: The Autoware Reference System evan.flynn@apex.ai

## Slide 2
What is a Reference System?
https://github.com/ros-realtime/reference-system

## Slide 3: Reference System
Simulates a real-world scenario rather than only a theoretical one
Enables repeatable tests that can be confirmed by many parties
Measures some set of performance metrics in order to compare results
https://github.com/ros-realtime/reference-system

## Slide 4: Reference System Base Node Types
Sensor Node
  input node to system
  one publisher, zero subscribers
  publishes message cyclically at some fixed frequency
Transform Node
  one subscriber, one publisher
  starts processing for N milliseconds after a message is received
  publishes message after processing is complete
Fusion Node
  2 subscribers, one publisher
  starts processing for N milliseconds after a message is received from all subscriptions
  publishes message after processing is complete
Cyclic Node
  N subscribers, one publisher
  cyclically processes all received messages since the last cycle for N milliseconds
  publishes message after processing is complete
Command Node
  prints output stats everytime a message is received
Intersection Node
  behaves like N transform nodes
  N subscribers, N publisher bundled together in one-to-one connections
  starts processing on connection where sample was received
  publishes message after processing is complete
https://github.com/ros-realtime/reference-system

## Slide 5: Reference Interfaces
One single message type is used for the entire system during each experiment run
This message type can be swapped depending on what is being measured
So far only one message type has been defined, but many more are waiting to be added
We store these message types in a package called Reference Interfaces
reference_interfaces/msg/Message4kb.idl
reference_interfaces/msg/TransmissionStats.idl
https://github.com/ros-realtime/reference-system

## Slide 6: Simulated (Pseudo) Work
Pseudo work is done by each node in the system in order to stress the system as in the real world
This pseudo work is done by finding prime numbers
  Starting from 3 since 0, 1 and 2 are not prime numbers
  Going up to some maximum value
Getting to this maximum value takes different amounts of time depending on the platform
To assist with this, a number_cruncher_benchmark program is provided
  outputs the time it takes your system to find all the prime numbers up to a maximum value
This maximum number sets how long each node will process for (aka “number crunch”)
Default maximum_number
https://github.com/ros-realtime/reference-system

## Slide 7
The Autoware Reference System
https://github.com/ros-realtime/reference-system

## Slide 8: The Autoware Reference System
Simulates the real-world structure of the Autoware.Auto Project
Uses all base node types
  Sensor, Transformer, Fusion, Cyclic, Command and Intersection
Has a signal path just like the real world that can be reliably tested
Front Lidar Driver -> Object Collision Estimator
https://github.com/ros-realtime/reference-system

## Slide 9
What can be measured?
https://github.com/ros-realtime/reference-system

## Slide 10: Key Performance Indicators (KPIs)
Latency of Front Lidar Driver/Rear Lidar Driver to the Object Collision Estimator
  Every lidar sample should cause the Object Collision Estimator to update
  Lower latency of the signal chain is better
Jitter of the timer for the Behavior Planner Cyclic Node
  Timer is supposed to trigger ever 100ms, but sometimes goes fast or slow depending on many things
  We can measure this jitter and report it
  Lower jitter and drift is better
Count the number of Dropped Samples
  Always use the latest samples - throw away old ones
  Lower number of dropped samples is better
CPU Utilization
  In general a lower CPU utilization is better since it enables you to choose a smaller CPU or implement more functionality
  Lower CPU utilization is better
Memory Utilization
  In general a lower memory utilization is better since it enables you to choose a smaller memory or have more space for other things
  Lower memory utilization is better
https://github.com/ros-realtime/reference-system

## Slide 11: Thank you! evan.flynn@apex.ai
https://github.com/ros-realtime/reference-system