## Slide 1
Priority-Driven Chain-Aware Scheduling with PiCAS
October 2021
roscon.ros.org/world/2021
Dr. Hyunjong Choi
Postdoc
University of California, Riverside

## Slide 2
roscon.ros.org/world/2021
Motivation
PiCAS framework
PiCAS on reference system

## Slide 3
Motivation
roscon.ros.org/world/2021

## Slide 4: Motivation
roscon.ros.org/world/2021
ROS 2 executor scheduling
< ROS2 architecture >
< Callback scheduling of executor† >
Timer callback
† D. Casini et al. “Response-time analysis of ROS 2 processing chains under reservation-based scheduling”, ECRTS, 2019
Executor
ready queue
CB
CB
CB
fetch
callback
CB
  Problems
  Suffers from priority inversion
  No systematic resource allocation methods
  Complex and pessimistic to analyze
  Difficult to prioritize critical chains

## Slide 5
PiCAS Framework
roscon.ros.org/world/2021

## Slide 6: PiCAS: Priority-driven Chain-Aware Scheduling framework for ROS2
roscon.ros.org/world/2021
Key idea: enables prioritization of mission-critical chains across complex abstraction layers of ROS 2
  To minimize end-to-end latency
  To ensure predictability even when the system is overloaded
PiCAS: Executor + Resource Allocation Algorithms + Timing Analysis
  PiCAS executor: priority-driven callback scheduling
  Resource allocation algorithms
    Callback Priority Assignment
    Chain-Aware Node-to-Executor Allocation
    Executor Priority Assignment
  Backed by formal end-to-end latency analysis

## Slide 7
roscon.ros.org/world/2021
PiCAS Algorithms
< Chain-aware scheduling strategies >
< Priority assignment >
< Node-to-Executor allocation >
< End-to-end timing analysis >
For details, please see our paper:
Hyunjong Choi, Yecheng Xiang, and Hyoseung Kim, PiCAS: New Design of Priority-Driven Chain-Aware Scheduling for ROS2. In IEEE Real-Time and Embedded Technology and Applications Symposium (RTAS), 2021. [ Paper | Slides | Video ]

## Slide 8
roscon.ros.org/world/2021
Implemented as an extension to the rclcpp wait-set executor
PiCAS executor API
PiCAS Executor (1/2)
client.hpp, service.hpp, timer.hpp, subscription_base.hpp, waitable.hpp
Default parameters
// Set RT priority and CPU affinity of executor instance
void Executor::set_executor_priority_cpu(int priority, int cpu);
// Enable/Disable priority-based callback scheduling
void Executor::enable_callback_priority();
void Executor::disable_callback_priority();
// Set callback priority
void Executor::set_callback_priority(rclcpp::TimerBase::SharedPtr ptr, int priority);
void Executor::set_callback_priority(rclcpp::SubscriptionBase::SharedPtr ptr, int priority);
void Executor::set_callback_priority(rclcpp::ServiceBase::SharedPtr ptr, int priority);
void Executor::set_callback_priority(rclcpp::ClientBase::SharedPtr ptr, int priority);
void Executor::set_callback_priority(rclcpp::WaitableBase::SharedPtr ptr, int priority);
// Spin for PiCAS (RT executor priority & CPU affinity)
void SingleThreadedExecutor::spin_rt();
class Executor
{ ...
#ifdef PICAS
bool callback_priority_enabled = false;
int executor_priority = 0;
int executor_cpu = 0;
...
#ifdef PICAS
int callback_priority = 0;
#endif
...
executor.hpp

## Slide 9
roscon.ros.org/world/2021
Implementation details
  Pro: waiting time for high-priority callback can be minimized
  Con: overhead; not good for high throughput of short, same-priority callbacks
PiCAS Executor (2/2)
Select the highest priority callback among all ready callbacks
Bool Executor::get_next_executable
{
bool success = false;
if (!success) {
wait_for_work(timeout);
}
success = get_next_ready_executable(any_executable);
...
}
get_next_executable of executor.cpp (PiCAS)
Update wait-set whenever each callback completes
Callbacks can be scheduled based on their priorities
Bool Executor::get_next_ready_executable
{
...
memory_strategy_->get_next_waitable(any_exe, weak_nodes);
if (any_exe.cb && highest_priority < any_exe.waitable->callback_priority) {
highest_priority = any_executable.waitable->callback_priority;
any_executable.timer = nullptr;
any_executable.subscription = nullptr;
any_executable.service = nullptr;
any_executable.client = nullptr;
}
else any_executable.waitable = nullptr;
...
}
get_next_ready_executable of executor.cpp (PiCAS)

## Slide 10
PiCAS on reference system
roscon.ros.org/world/2021

## Slide 11
roscon.ros.org/world/2021
PiCAS on reference system
Clone our forked repository
Build with PiCAS executor
  Use PICAS CMake variable
Configuration change for Linux RT priority
  Modify /etc/security/limits.conf
Notes
  PiCAS is implemented as an extension to rclcpp, located in reference-system/rclcpp. This local rclcpp overrides the default ROS2 rclcpp.
  If -DPICAS=FALSE, reference-system/rclcpp is exactly the same as the ROS2 Galactic version.
git clone https://github.com/rtenlab/reference-system.git
colcon build --cmake-args -DRUN_BENCHMARK=TRUE -DTEST_PLATFORM=TRUE -DPICAS=TRUE
<userid> hard rtprio 99
<userid> soft rtprio 99

## Slide 12
roscon.ros.org/world/2021
How to use PiCAS executor
Declaration of executor
Enable callback priority (PiCAS executor)
Set executor’s real-time priority and assign CPU
Executor (process) scheduled under SCHED_FIFO policy that has a sched_priority value in the range 1 (low) to 99 (high).
Allocate nodes to executor
Run executor (spin_rt())
callback_priority_enabled = true
std::thread spinThread(&rclcpp::executors::SingleThreadedExecutor::spin_rt, &executor);
autoware_default_singlethreaded_picas_single_executor.cpp

## Slide 13
Callback priority assignment on reference system
Or, use API, e.g.,
roscon.ros.org/world/2021
How to assign callback priority
reference_system/include/reference_system/nodes/rclcpp/nodes.hpp
autoware_reference_system/include/autoware_reference_system/autoware_system_builder.hpp
autoware_reference_system/system/priority/default.hpp
Set unique priority to callbacks
executor.set_callback_priority(node->callback, priority)

## Slide 14
roscon.ros.org/world/2021
Evaluation
Autoware model
Single executor instance & multiple executor instances
  Based on the PiCAS priority assignment and node-to-executor allocation algorithms
  Algorithm implementation: https://github.com/rtenlab/ros2-picas
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
: Criticality of chains
>
>
Number (the higher, more critical)
: Priority of callback
: hot topic path (latency is the one of KPIs)

## Slide 15
roscon.ros.org/world/2021
Evaluation
Experiment environment
  Raspberry Pi 4 with fixed CPU frequency of 1.5GHz
  4 CPU cores for multiple executors (PiCAS) and multithreaded executor (ROS2 default)
  Run with RUN_TIMES option of 60 seconds
  Evaluation criteria : Key Performance Indicators (KPIs) of reference system
colcon test

## Slide 16
roscon.ros.org/world/2021
Evaluation
Latency summary
PiCAS-single
executor
PiCAS-multiple executors
Default-single threaded
Default-multi threaded
Default-static singlethreaded

## Slide 17
roscon.ros.org/world/2021
Evaluation
Dropped messages summary
PiCAS-single
executor
PiCAS-multiple executors
Default-single threaded
Default-multi threaded
Default-static singlethreaded

## Slide 18
roscon.ros.org/world/2021
Evaluation
Behavior planner jitter
PiCAS-single
executor
PiCAS-multiple executors
Default-single threaded
Default-multi threaded
Default-static singlethreaded

## Slide 19
roscon.ros.org/world/2021
Evaluation
CPU usage summary
Memory usage summary
PiCAS-single
executor
PiCAS-multiple executors
Default-single threaded
Default-multi threaded
Default-static singlethreaded
PiCAS-single
executor
PiCAS-multiple executors
Default-single threaded
Default-multi threaded
Default-static singlethreaded

## Slide 20
roscon.ros.org/world/2021
Thank you
Q & A
https://github.com/rtenlab/reference-system